Ht202211 AirPort base stations About AirPort base station status lights LED

Learn about AirPort base station status lights (LED).

The Status Lights on AirPort base stations provide status information about the current state of the AirPort base station through a series of colors and/or flashing patterns. The Status light is also referred to as an LED.

All newer AirPort Extreme and AirPort Time Capsule base stations have a single status light that can change to amber, green, or blue.

When you connect power to your AirPort base station, the status light flashes green for one second and then amber while your AirPort base station starts up. After your AirPort base station has started up completely, the status light flashes amber until your AirPort base station has been updated with the correct settings. The status light glows solid green after your AirPort base station is properly set up and connected to the Internet or a network. When you connect Ethernet cables to the Ethernet ports, the lights above them glow solid green.

AirPort Extreme, AirPort Time Capsule (802.11 a/b/g/n)

| Status light | Description |
| --- | --- |
| Off | No power |
| Solid amber | Completing the startup sequence |
| Solid green | Working normally |
| Solid blue | Ready to allow a wireless client access to the network via Wi-Fi Protected Setup (WPS). AirPort Utility will indicate that the status light is solid green. |
| Flashing green | If you choose Flash On Activity from the Status Light pop-up menu (in the Base Station pane of AirPort settings in AirPort Utility), the status light will flash green to indicate normal activity. |
| Flashing amber | Startup is complete, but the Wi-Fi base station has detected a condition that requires your assistance. To resolve flashing amber status light conditions click here to learn more. Launch AirPort Utility to find out what conditions are being reported. |
| Alternating amber/green | When multiple Wi-Fi base stations are available during setup, you can trigger this behavior by using the Identify feature in AirPort Utility. |

AirPort Express 802.11n (2nd Generation)

There is a single status light that can change to amber, or green.

When you connect power to your AirPort Express base station, the status light flashes green for one second and then amber while your AirPort base station starts up. After your AirPort base station has started up completely, the status light flashes amber until your AirPort base station has been updated with the correct settings. The status light glows solid green after your AirPort base station is properly set up and connected to the Internet or a network. When you connect Ethernet cables to the Ethernet ports, the lights above them glow solid green.

| Status light | Description |
| --- | --- |
| Off | No power |
| Solid amber | Completing the startup sequence |
| Solid green | Working normally |
| Flashing green | If you choose Flash On Activity from the Status Light pop-up menu (in the Base Station pane of AirPort settings in AirPort Utility), the status light will flash green to indicate normal activity. |
| Flashing amber | Startup is complete, but the Wi-Fi base station has detected a condition that requires your assistance. To resolve flashing amber status light conditions click here to learn more. Launch AirPort Utility to find out what conditions are being reported. |

AirPort Express (802.11a/b/g)

The original AirPort Express (802.11 a/b/g) Wi-Fi base station has a single status light that can change to amber, yellow, or green.

When you connect power to your AirPort Express, the status light flashes green for one second and then amber while it starts up. After the AirPort Express has completed startup, the status light flashes amber until the AirPort Express has been updated with the correct settings. The status light glows solid green after the AirPort Express is properly set up and connected to the Internet or a network.

| Status light | Description |
| --- | --- |
| Off | No power |
| Solid amber | Completing the startup sequence |
| Solid green | Working normally |
| Flashing green | If you choose Flash On Activity from the Status Light pop-up menu (in the Base Station pane of AirPort settings in AirPort Utility), the status light will flash green to indicate normal activity. |
| Flashing amber | Startup is complete, but the AirPort Express has detected a condition that requires your assistance. To resolve flashing amber status light conditions click here to learn more. Launch AirPort Utility to find out what conditions are being reported. |
| Alternating amber/green | When multiple Wi-Fi base stations are available during setup, you can trigger this behavior by using the Identify feature in AirPort Utility. |

AirPort Base Station (802.11 b/g)

The AirPort Extreme Base Station (802.11 b/g) has three white LED lights that do not change colors.

When you connect power to your AirPort Base Station (802.11 b/g), the three status lights will alternately flash in a sequence from right to left. This indicates that the base station is starting up.

| Left | Center | Right | Status/Description |
| --- | --- | --- | --- |
| Off | Off | Off | No power |
| On | Off | On | The base station is in self-check mode. |
| Flashing | Flashing | Flashing | Failed the power-on self-test. Contact your Apple-authorized service provider. |
| Off | Flashing slowly | Off | Soft reset mode1. |
| Off | Flashing three times | Off | Hard reset mode1. |
| Off/flashing | On | Off/Flashing | Left and right flashing indicates normal network activity. The left LED flashing indicates AirPort wireless activity and the right LED flashing indicates Ethernet or modem activity. |

Learn more

1Click here more information about resetting your base station.

Occasionally, the LED on the AirPort Express may flash once when starting up and not again after that. If this occurs, hard reset it. If the LED continues to flash only once at startup, the AirPort Express should be serviced.

Helpful?

Yes No

Article:

HT202211

Last Modified:

05/13/2016

Affected Products:

AirPort Extreme 802.11n (1st Generation),AirPort Extreme 802.11n (2nd Generation),AirPort Time Capsule 802.11n (1st Generation),AirPort Time Capsule 802.11n (2nd Generation),AirPort Time Capsule 802.11n (3rd Generation)

Related

How To

- Resetting an AirPort base station FAQ   Wi-Fi base station: Understanding and resolving a blinking amber status light   AirPort base stations: Can't add additional AirPort base stations to an extended network if MAC Address Access Control is enabled   Wi-Fi base stations: How to set up and configure AirPort Express for AirPlay and iTunes   AirPort Utility: Monitor base stations for problems   AirPort Base Station: ISP provisioning may prevent Internet connection via broadband (cable or DSL)   AirPort base stations: How to find the Wi-Fi network when it doesn't appear normally   AirPort base stations: Setting up and configuring an extended wireless network (802.11n)

Manuals

Apple AirPort Networks