Ht204291 Get help with AirPlay and AirPlay Mirroring on your iPhone iPad or iPod touch

If you can't mirror or stream content from your iOS device to your Apple TV or other AirPlay enabled device, learn what to do.

Check for updates and compatibility issues

- Make sure that you have the latest software on your iOS device and Apple TV.

- Check for device compatibility: You can AirPlay content only to an Apple TV or AirPlay enabled speaker or receiver. (You can't AirPlay content from your iOS device to another iOS device or to a Mac.)

If you still need help, follow the steps for your issue:

AirPlay unavailable  or see Apple TV alert

Don't see your AirPlay device  in Control Center

Can't stream iTunes  or 3rd party content

See video but can't hear audio

Interrupted content or lagging network

If you don't see AirPlay options in Control Center or a message says, "Looking for Apple TV"

When an AirPlay enabled device is available, you should see AirPlay options in Control Center on your iOS device. For example, open Control Center on your iOS device. Then look for AirPlay Mirroring or swipe to find the Now Playing screen that lists available AirPlay devices:

If you can't find AirPlay options or you see a "Looking for Apple TV" message, follow these steps:

- Restart your iOS device and Apple TV (or other AirPlay enabled device).

- If your Apple TV uses Ethernet,* check that the cable is plugged into the router that you use for Wi-Fi.

- On your iOS device, go to Settings > Wi-Fi and check that you're on the same Wi-Fi network as your Apple TV or other AirPlay enabled device.

- Then check the Wi-Fi network on your Apple TV (or other AirPlay enabled device):

  - For Apple TV (4th generation), go to Settings > Network and check that you're on the same Wi-Fi network as your iOS device.

  - For Apple TV (2nd or 3rd generation), go to Settings > General > Network.

- On your Apple TV, make sure that AirPlay is turned on in Settings > AirPlay.

- If you still need help, contact Apple Support.

* If your Apple TV is in Sleep mode and uses Ethernet, you need to wake your Apple TV with a remote before you can AirPlay content.

If you don't see the device you want to stream to

Open Control Center on your iOS device and swipe horizontally to find the Now Playing screen. You should see a list of devices that you can AirPlay to.

Don't see the AirPlay device that you need? Here's what you should check:

- Make sure that you plug in and turn on the AirPlay device that you want to stream to.

- If you're streaming to an Apple TV, make sure that AirPlay is turned on in Settings > AirPlay.

- If your Apple TV uses Ethernet,* check that the cable is plugged into the router that you use for Wi-Fi.

- On your iOS device, go to Settings > Wi-Fi and check that you're on the same Wi-Fi network as your Apple TV or other AirPlay device.

- Check the same thing on your Apple TV (or other AirPlay device):

  - For Apple TV (4th generation), go to Settings > Network. Check that you're on the same Wi-Fi network as your iOS device.

  - For Apple TV (2nd or 3rd generation), go to Settings > General > Network. Check that you're on the same Wi-Fi network as your iOS device.

- If you still need help, contact Apple Support.

* If your Apple TV is in Sleep mode and uses Ethernet, you need to wake your Apple TV with a remote before you can AirPlay content.

If you can't stream iTunes Store or third-party content

- To stream iTunes Store content and some other types of content, your Apple TV needs an Internet connection. Check your connection and try again.

- To AirPlay rented content, wait for it to download completely. Sometimes you can't AirPlay rental content until it fully downloads.

- For the app you're using, check its product page or website to see whether the app supports AirPlay. Without support for AirPlay video playback, an app might not be able to stream video.

- Get help using AirPlay with iTunes.

If you see video but don't hear audio

- Make sure that the volume is up (not muted) on both your iOS device and your television or receiver.

- On your iPhone or iPad, check the Ring/Silent switch. If it's set to silent, you'll see an orange line. Toggle the switch to turn on the ringer.

If your content gets interrupted or your network lags

If you have a weak Wi-Fi signal or interference from a nearby device, like a microwave or baby monitor, follow these steps:

- Make sure that you use the recommended settings for your Wi-Fi router.

- Move or turn off other devices that might cause interference.

- If possible, connect your Apple TV directly to your router with an Ethernet cable instead of using Wi-Fi.

Your AirPlay connection might get interrupted when you lock your device, put it to sleep, or switch to a different app.

When to try Peer-to-Peer AirPlay

If a customers wants to use AirPlay on a Wi-Fi network that has limited or no Internet connectivity, Peer-to-Peer AirPlay might work instead(However, some content providers, like iTunes and certain third parties, require Internet connectivity on the Apple TV in order to use AirPlay).

With peer-to-peer AirPlay, an iOS device and Apple TV don't have to be on the same Wi-Fi network. Make sure that both devices have Wi-Fi and Bluetooth turned on. To use peer-to-peer AirPlay, you need one of these devices with iOS 8 or later:

- iPhone 5 or later

- iPad mini or iPad (4th generation) or later

- iPod touch (5th generation) or later

You can stream content to your Apple TV (3rd generation rev A, model A1469 or later).

All AirPlay RTAs should include the following information:

- AirPlay from device (e.g. iPhone) model, serial number, software version:

- AirPlay to device (e.g. Apple TV) model, serial number, software version:

- What specifically happens when the customer attempts to use AirPlay?

- What type of content is being AirPlayed? (personal content, purchased content, or screen of a device)

- How does the customer activate AirPlay? (Control Center, AirPlay button within a specific app, etc)

- Is the customer using AirPlay or AirPlay Mirroring?

- Is Bluetooth enabled?

Be prepared to provide the following details:

- With what OS version did the issue begin?

- How far is the iOS device to the wireless router or access point?

- How far is the iOS device to the Apple TV or AirPlay speaker?

- Wireless router make and model:

- Network security type (WEP, WPA2, etc):

- Router / AP firmware version:

- Are the Apple TV and iOS device / Mac connected to the same network name?

- Does the customer have additional access points, routers, repeaters, or other network equipment?  If so, please provide make, model, and topology:

Helpful?

Yes No

Article:

HT204291

Last Modified:

12/28/2016

Radar Number:

22427311, 27062154 View >

Open tickets in radar

Affected Products:

Apple TV (2nd generation),Apple TV (3rd generation),Apple TV (4th generation)

Related

How To

Use AirPlay or AirPlay Mirroring on your iPhone, iPad, or iPod touch   iTunes: About playing music with AirPlay   Use AirPlay to display video from your Mac on an HDTV   iOS: Use AirPlay Mirroring   Resolve issues with AirPlay and AirPlay Mirroring from iPhone, iPad, and iPod touch   Sync your iPhone, iPad, or iPod touch with iTunes using Wi-Fi   Connect your Mac to a home stereo, iPod, iPad, musical instruments, or speakers   Wi-Fi base stations: How to set up and configure AirPort Express for AirPlay and iTunes   iPhone, iPad, and iPod touch: Set up a dispatch, exchange, repair, or replacement for hardware issues only