# HT204371 AirPort Express: What is client mode?

When talking about a Wi-Fi network, a "client" is simply something that joins the network, like your computer. A client could also be a wireless print server or wireless audio device.

AirPort Express can function as a full-fledged wireless access point, or it can join an existing network just to offer its wireless print server and audio features. When AirPort Express does that, it is in "client mode."

In client mode, AirPort Express does not offer itself as a wireless access point or use its Ethernet port. As a wireless client, AirPort Express is simply a destination for AirTunes and print jobs. It can join both 802.11b and 802.11g networks, including those using security features such as WEP and WPA-PSK.

In client mode, the ProxySTA feature allows wired clients to be connected via Ethernet (with 802.11n-based AirPort Express only).

Wireless Distribution System is another way for AirPort Express to join an existing Wi-Fi network. AirPort Express uses its Ethernet port and can offer its wireless access point in WDS mode, but it requires that your other access points be AirPort Extreme and/or AirPort Express. Client mode's advantage is that you can join the networks of non-Apple access points and earlier AirPort base stations ("Dual Ethernet" and "Graphite" models).

## Learn more

Other Wi-Fi product manufacturers have different names for "client mode." These include "client station mode," "AP client mode," "wireless client mode," and "STA mode." Whenever one of these modes is required, just remember that "client mode" is the same thing.

Helpful?

Yes  No

Article:

HT204371

Last Modified:

05/13/2016

Affected Products:

AirMac Express with 802.11n-JP,AirPort Express 802.11n (1st Generation)

#### Related

##### How To

- AirPort Express: How to join an existing Wi-Fi network in client mode

- AirPort Express frequently asked questions (FAQ)

- Wi-Fi base stations: How to set up and configure AirPort Express for AirPlay and iTunes

- Wi-Fi base stations: Extending the range of your wireless network by adding additional Wi-Fi base stations

- AirPort Express: Difficulty joining third-party network that is using WEP

- AirPort Utility: Reserve a DHCP address for client computers

- Gather log files from customers for macOS

- Help customers with Wi-Fi networks and connections in iOS

- Wi-Fi: Guest network clients can communicate with each other, but cannot connect to the Internet