PH22800 AirPort Utility Set up a guest network

You can set up a guest network that segregates a portion of your Internet traffic away from the main network.

Set up a guest network

- Open AirPort Utility, located in the Utilities folder in the Applications folder.

- In the graphical overview, select the base station you want to set up, then click Edit. You may need to enter a password for the base station.

- Click Wireless.

- Select Enable Guest Network, then optionally change the default guest network name.

- Click the Guest Network Security pop-up menu, then choose one of the following options:

  - None: Choose this option if you want your network to have no security and be open to all users.

  - WPA/WPA2 Personal: This is the recommended security level. Choose this option if you want computers compatible with WPA and WPA2 to join your network.

  - WPA2 Personal: Choose this option if you only want WPA2-compatible computers to join your network.

- If you selected WPA/WPA2 Personal or WPA2 Personal, enter a password in the Guest Network Password and Verify Password fields.

- When you’re done, click Update to save your changes.

Extend your guest network

If your network uses more than one base station, you can extend your guest network.

- To identify the base station that is configured as a router, do the following:

  - In the graphical overview, select a base station, then click Edit. You may need to enter a password for the base station.

  - Click Network, then confirm that the router mode is set to “DHCP and NAT.”

- On the router base station, click Wireless.

- Select Enable Guest Network, then optionally change the default guest network name.

- Click the Guest Network Security pop-up menu, then choose one of the following options:

  - None: Choose this option if you want your network to have no security and be open to all users.

  - WPA/WPA2 Personal: This is the recommended security level. Choose this option if you want computers compatible with WPA and WPA2 to join your network.

  - WPA2 Personal: Choose this option if you only want WPA2-compatible computers to join your network.

- If you selected WPA/WPA2 Personal or WPA2 Personal, enter a password in the Guest Network Password and Verify Password fields.

- On each remaining extender base station in your network, enable the guest network by doing the following:

  - In the graphical overview, select the base station, then click Edit. You may need to enter a password for the base station.

  - Click Wireless, click the Network Mode pop-up menu, then choose “Extend a wireless network.”

  - Verify that the wireless security mode and passwords match the guest network configuration on the router base station.

- When you’re done, click Update to save your changes.

SEE ALSO

Change your base station’s name and password

If you forget your base station or Wi-Fi password

Apple Support article: Guest mode isn‘t available with some IPv6 configurations on AirPort devices

Helpful?

Yes No

Article:

PH22800

Last Modified:

03/31/2017

Related

How To

AirPort Utility 6.x: Set up a guest network   AirPort Express: Difficulty joining third-party network that is using WEP   Wi-Fi base stations: How to set up and configure AirPort Express for AirPlay and iTunes   Wi-Fi base stations: Setting up and configuring a roaming network (802.11 a/b/g/n)   AirPort base stations: Setting up and configuring an extended wireless network (802.11n)   Setting up Time Capsule for the first time   AirPort Utility: Share an Internet connection with multiple computers   AirPort Utility 6.x: Set DHCP options for your base station or your AirPort Time Capsule   AirPort Express frequently asked questions (FAQ)